## Slide 1: Octopus Timer
Nov. 15, 2019 (original)
Dec. 2, 2019 (updated, first release)
Jan 22, 2020 (added trigger/gate selection and module reg slides)
Feb 27, 2020 (added 2 more examples at end)

## Slide 2: Timer requirements
Better than 1us resolution [10ns planned]
Delays up to at least ~3sec (wc stage movement time per voxel)
SW-configurable (E.g. select trigger source and level/edge, GPIO for output, program delays, etc. without having to recompile the Verilog)
Duplicate existing functionality:
  Trigger to pulse (high or low)
  Trigger to N pulse cycles (N >= ~1M):
  Himax double-pulse:
  Ability to sync all timers to global source
  Ability to gate the trigger (level sensitive) with an external signal
trigger
d
d
w1
w2
d
w1
w2
w1

## Slide 3: Timer functionality (generalized)
From trigger, assume the timer needs a specific delay to properly synchronize its first edge with all of the other timer outputs, thereafter we might have to issue some number of possibly gated single or double-pulses before either stopping or awaiting another trigger:
At the end of each programmed delay, we can continue to the next delay, wait for a trigger, or end
End (stay at constant value)
Or wait for another trigger
d1
d2
trigger
d3
d4
d5
(optional)
trigger
(optional)
trigger

## Slide 4: Timer state machine: state functionality
(this state) count<=1 &&
(next state) gate&trigger==1
transition_count <= transition_count -1
If( transition_count == 0)
state =end_state
else
state = next_state
Allow each state to use trigger or not, count down delay, output value, and next state
state
out <= state_output_value
count <= count – 1;
en==0
state = start_state
count>1 ||
(next state) gate&trigger==0
(prior state)count<=1 && (this state) gate&trigger==1
Note: trigger for state gates entry into that state – prior state will either hold until trigger is seen and count<=1 (use_trigger==1) or will transition automatically on count<=1 (use_trigger==0)
Note: we also count transitions between states to count out N ‘pulses’
(Program to N*# of states/’pulse’)

## Slide 5: Timer state machine
State 4
State 6
State 1
State 2
enabled
&&
Trigger&gate state1
Start
(State 0)
End
(State 7)
!enabled
count>1
|| !trigger&gate
transition_count==0
|| next_state==end
enabled
!enabled
!enabled
State 3
State 5

## Slide 6: Timer trigger/gate selection
Trigger (and gate) selection are as follows:
select = 0:7 → GPIO_IN[0:7] (or 1:8 as labeled on board)
select = 8:23 → GPIO_OUT[0:15] (or 1:16 as labeled on board)
Note GPIO_OUT[1:16] = Timer[1:16]
select = 24:30 → Hard-coded to 0
select = 31 → Hard-coded to 1
Trigger sense: Gate sense:
0 (2’b00) is level sensitive low 0 level sensitive low
1 (2’b01) is edge sensitive rising 1 level sensitive high
2 (2’b10) is edge sensitive falling
3 (2’b11) is level sensitive high

## Slide 7: Timer module I/O
// Input ports
input clk;
input en;
input [4:0] trigger_select;
input [1:0] trigger_sense;
input [4:0] gate_select;
input gate_sense;
input start_output_value;
input s1_output_value;
input s1_use_trigger;
input [31:0] s1_count;
input [2:0] s1_next_state;
input s2_output_value;
input s2_use_trigger;
input [31:0] s2_count;
input [2:0] s2_next_state;
input s3_output_value;
input s3_use_trigger;
input [31:0] s3_count;
input [2:0] s3_next_state;
input s4_output_value;
input s4_use_trigger;
input [31:0] s4_count;
input [2:0] s4_next_state;
input s5_output_value;
input s5_use_trigger;
input [31:0] s5_count;
input [2:0] s5_next_state;
input s6_output_value;
input s6_use_trigger;
input [31:0] s6_count;
input [2:0] s6_next_state;
input end_output_value;
input [31:0] state_transition_count;
input [7:0] gpio_in;
input [15:0] gpio_out;
output out;
timer registers

## Slide 8: Timer top
timer.v
clk
en
enable
start, end
state1
state2
state3
state4
state5
trigger,gate sense
out
clk
reset
timer_top.v
Ctrlr
Intf
To master
controller
interface
trigger
GPIO_IN
registers
register
state
gateselect
triggerselect
transition count
gate
GPIO_OUT
state6
out

## Slide 9: Timer top (Module Registers)
// Register address map: Address[0]
assign trigger_select = reg_addr0[4:0]; // 5b
assign trigger_sense = reg_addr0[6:5]; // 2b
assign gate_select = reg_addr0[11:7]; // 5b
assign gate_sense = reg_addr0[12];
assign start_output_value = reg_addr0[13];
assign end_output_value = reg_addr0[14];
// unused reg_addr0[15]
// Register address map: Address[1]
assign s1_output_value = reg_addr1[0];
assign s1_use_trigger = reg_addr1[1];
assign s1_next_state = reg_addr1[4:2]; // 3b
assign s2_output_value = reg_addr1[5];
assign s2_use_trigger = reg_addr1[6];
assign s2_next_state = reg_addr1[9:7]; // 3b
assign s3_output_value = reg_addr1[10];
assign s3_use_trigger = reg_addr1[11];
assign s3_next_state = reg_addr1[14:12]; // 3b
// unused reg_addr1[15]
// Register address map: Address[2] and [3]
assign s1_count = {reg_addr3[15:0], reg_addr2[15:0]};
// Register address map: Address[4] and [5]
assign s2_count = {reg_addr5[15:0], reg_addr4[15:0]};
// Register address map: Address[6] and [7]
assign s3_count = {reg_addr7[15:0], reg_addr6[15:0]};
// Register address map: Address[8]
assign s4_output_value = reg_addr8[0];
assign s4_use_trigger = reg_addr8[1];
assign s4_next_state = reg_addr8[4:2]; // 3b
assign s5_output_value = reg_addr8[5];
assign s5_use_trigger = reg_addr8[6];
assign s5_next_state = reg_addr8[9:7]; // 3b
assign s6_output_value = reg_addr8[10];
assign s6_use_trigger = reg_addr8[11];
assign s6_next_state = reg_addr8[14:12]; // 3b
// unused reg_addr8[15]
// Register address map: Address[9] and [10]
assign s4_count = {reg_addr10[15:0], reg_addr9[15:0]};
// Register address map: Address[11] and [12]
assign s5_count = {reg_addr12[15:0], reg_addr11[15:0]};
// Register address map: Address[13] and [14]
assign s6_count = {reg_addr14[15:0], reg_addr13[15:0]};
// Register address map: Address[16] and [15]
assign state_transition_count = {reg_addr16[15:0], reg_addr15[15:0]};
Each timer module has 17 (addressed 0:16) registers of short (16-bit) length.
To program timer state, write these 17 registers and enable the module to begin operation.

## Slide 10: Example: One-shot
E.g. Enabling timer gets 1 output pulse. Disabling returns to low/start.
trigger_select = 31; // = 1 (will always trigger with level high sense)
trigger_sense = 3; // 1 = 2’b11, i.e. level sensitive high
gate_select = 31; // addr 31 is always ‘1’
gate_sense = 1; // so gate is always allowing trigger through
start_value = 0;
s1_use_trigger = 0; // don’t wait for trigger
s1_output_value = 1; // output high in this state
s1_count = 1e6; // e.g. say 1ms (10ns steps) until sync’ed
s1_next_state = 7; // end is next
transition_count = 1e9; // Just has to be > 1
end_value = 0; // or make this 1 to make it stay high
Hjyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyyymnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnnjmjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjjgfv c
Start
End
Upon enabling Timer,
goes to state1
Disable goes back
to start
State 1
After 1ms
1ms

## Slide 11: Example: delayed double-pulse from trigger
E.g. 2 pulses after every trigger
trigger_select = GPIO_INPUT_2; // e.g. say this comes from laser
trigger_sense = 1; // 1 = 2’b01, i.e. 0->1 (rising edge)
gate_select = 31; // addr 31 is always ‘1’
gate_sense = 1; // so gate is always allowing trigger through
start_value = 0;
s1_use_trigger = 1; // enter state1 after trigger event
s1_output_value = 0; // output low in this state
s1_count = 1.6e6; // e.g. say 16ms (10ns steps) until sync’ed
s1_next_state = 2; // state2 is next
s2_use_trigger = 0; // do not wait on trigger, continue
s2_output_value = 1; // go high
s2_count = 0.5e6; // e.g. say 5ms high
s2_next_state = 3; // state3 is next
s3_use_trigger = 0; // do not wait on trigger, continue
s3_output_value = 0; // go low
s3_count = 1.0e6; // e.g. say 10ms low
s3_next_state = 4; // continue to state4
s4_use_trigger = 0; // do not wait on trigger, continue
s4_output_value = 0; // go high
s4_count = 1.5e6; // e.g. say 15ms high
s4_next_state = 5; // continue to state5
s5_use_trigger = 0; // do not wait on trigger, continue
s5_output_value = 0; // go low
s5_count = 2.0e6; // e.g. say 20ms low
s5_next_state = 0; // loop back to start to wait for next trigger
transition_count = 1e9; // don’t use/need for this, set to big num
State 1
State 2
State 3
Start
GPIO_INPUT_2
Triggers 0->1
16ms
5ms
10ms
After 16ms
After 5ms
State 4
State 5
After 10ms
15ms
20ms
16ms
5ms
After 15ms
After 20ms

## Slide 12: Example: N cycles output from trigger (once)
E.g. N=6 cycles of pulse/clock
trigger_select = GPIO_INPUT_2; // e.g. say this comes from laser
trigger_sense = 1; // 1 = 2’b01, i.e. 0->1 (rising edge)
gate_select = 31; // addr 31 is always ‘1’
gate_sense = 1; // so gate is always allowing trigger through
start_value = 0;
s1_use_trigger = 1; // enter state1 after trigger event
s1_output_value = 0; // output low in this state
s1_count = 1.6e6; // e.g. say 16ms (10ns steps) until sync’ed
s1_next_state = 2; // state2 is next
s2_use_trigger = 0; // do not wait on trigger, continue
s2_output_value = 1; // go high
s2_count = 0.5e6; // e.g. say 5ms high
s2_next_state = 3; // state3 is next
s3_use_trigger = 0; // do not wait on trigger, continue
s3_output_value = 0; // go low
s3_count = 0.5e6; // e.g. say 5ms low
s3_next_state = 2; // loop back to state2
transition_count = 13; // 1+N*2 for N=6 pulses
end_value = 0;
State 1
State 2
State 3
Start
End
GPIO_INPUT_2
Triggers 0->1
16ms
5ms
5ms
After 16ms
After 5ms
After 5ms
transition_count==0

## Slide 13: Example usage: Pulse swallowing
Say we have a signal with 50% duty cycle at Tperiod where we want to output a pulse at (N+1)* Tperiod :
Set state1 high (or low) for 0.5* Tperiod and state2 low (or high) for N *Tperiod
Set state1 to use_trigger to await a rising (or falling) edge from the signal
Set state2 not to use_trigger.
Set state1 to transition to state2 and state2 to transition back to state1
Set the state_transition_count to be 2x how many cycles you want to do this
signal
e.g. N=1
e.g. N=2
state1
state2
state2
awaiting
trigger
state1
state1
state2
state2
awaiting
trigger
etc.
etc.
state1